## Slide 1: 16-bit RO Physical Unclonable Function ---EEL4720 Final Project
Shida yang
Beichen Su

## Slide 2: Table of Content
  Introduction to the application
  Design and Implementation
  Testing and demonstration
  Test Results
  Problem Encountered

## Slide 3: Introduction
Nowadays, people rely more and more on their digital devices, which stored so many important privacy information like radio-frequency identification (RFID). Hardware security is becoming increasingly important.
Our application is mainly focused on hardware authentication

## Slide 4: Introduction
In traditional methods, secret keys are stored digitally in a nonvolatile memory which is always vulnerable based on hardware implementation and key storage.
For extremely resource contained platform such as radio-frequency identification (RFID), even simple cryptographic operations can be too costly.
Software-only protection is not enough. Non-volatile memory technologies are vulnerable to invasive attack as secrets always exist in digital form.
  adversaries can physically extract secret keys from EEPROM while processor is off
Due to the differences between each devices (length, width, oxide thickness) in circuit and system (Process Variation), each IC has unique properties.

## Slide 5: Introduction
Physical Unclonable Function (PUF) is a function that is:
  Based on a physical system
  Easy to evaluate (using the physical system)
  Outputs looks like random function
  Unpredictable even for an attacker with physical access
Path delays in an IC are statistically distributed due to random manufacturing variations

## Slide 6: Introduction
Ring-Oscillator (RO) PUF replies on delay loops and counters instead of MUX and arbiters because it will be more stable on FPGA.
Our design is implementing a 16-bit RO PUF. Input (Challenge) is 16 bit and the output is 1 bit. We store 32 different 16-bit challenges, generated by a random generator function, in RAM and pass through all challenges one by one to form a 32-bit response sequences.

## Slide 7: Design and Implementation

## Slide 8: Design and Implementation

## Slide 9: Test and Demo (Method and Goal)
We will use intra-Hamming Distance and inter-Hamming Distance to test our design.
What is Hamming Distance?
  Given two numbers, calculate the fraction of bits that are different
  For example, use two 8-bit number
    0b11001010
    0b10001011
    2 different bits, so HD=2/8=0.25

## Slide 10: Test and Demo (Method and Goal)
Intra-HD
  Give same set of input to the same chip multiple times
  Compare the HD between the outputs
  Tells how reliable the design is
  Ideally close to 0 because a reliable design should have the same output for the same input
Inter-HD
  Give same set of input to different chips
  Compare the HD between the outputs across chips
  Tells how unique each chip is when implementing the same design
  Ideally close to 0.5 because each bit has two possible outcomes, so half of the bits should be different on average

## Slide 11: Test and Demo (Data and Control Flow)

## Slide 12: Test and Demo (main.cpp – Input/Output)

## Slide 13: Test and Demo (main.cpp – Intra-HD)
  25 outputs in the same test from 25 trials
    Output 0 ~ Output 24
  Pairing output (every possible combination)
    Output 0 – Output 1, Output 0 – Output 2, Output 0 – Output 3, Output 0 – Output 4, …Output 0 – Output 23, Output 0 – Output 24
    Output 1 – Output 2, Output 1 – Output 3, Output 1 – Output 4, …Output 1 – Output 23, Output 1 – Output 24
    Output 2 – Output 3, Output 2 – Output 4, … Output 2 – Output 23, Output 2 – Output 24
    ……
    Output 23 – Output 24
  For each pair, calculate intra-HD
    Find number of different bits (n), divide by total number of bits (32)
    n/32
  Average the intra-HDs

## Slide 14: Test and Demo (top.cpp – Inter-HD)
  Keep doing test until get results from two different boards
  25 outputs from board 1, 25 outputs from board 2
  Pair them up just like in the previous slide
    First element in the pair is from board 1, second element is from board 2
  For each pair, calculate inter-HD
    Find number of different bits (n), divide by total number of bits (32)
    n/32
    Same algorithm for calculating Hamming Distance, just the pairs are from different boards
  Average the inter-HDs

## Slide 15: Test and Demo (Command Line)
  ./top.o RAND_SEED INTRA_OR_INTER
    RAND_SEED: make sure the same set of input is given to the board
    INTRA_OR_INTER: 0=inter-HD, 1=intra-HD
  Printed Result
    6 tests, each test is the average of 25 trials

## Slide 16: Result (Intra-HD)

## Slide 17: Result (Inter-HD)
  The average inter-HDs we measured from our boards are far from ideal
    Should be around 0.5 ideally
    Our data ranges from 0.03 to 0.18
    The implemented design favors certain ROs over others (explained in the next slide)

## Slide 18: Problem Encountered
Each Ring-Oscillator is routed differently internally
  Example: RO_0 and RO_128
  RO_0 is in the first mux
  R0_128 is in the second mux
  Routing lengths are different (RO_128 looks shorter)
  If a challenge is 0b1000000000000000
  The output would favor second mux in either board
Need to find a way to place internal routing for all the ROs equally

## Slide 19: Conclusion
We build a 16-bit Ring Oscillator Physical Unclonable Function with great complexity in both hardware structure and software algorithm, which can be used in hardware security protection in the real world.
Currently it is highly reliable but not so special for each devices, we are satisfied about our progress and result so far.
We will still try to find a way to manipulate the structure of the hardware to make it perfectly match, we hope to get some advice from you.